## Slide 1: Anomaly Detection of Building Energy Consumption using Forecasting Techniques
Spring 2019, AE Research Project Proposal
ASDL, Georgia Institute of Technology
Kunal Sharma. January 25, 2019

## Slide 2: Problem Statement
“Typical Buildings Consume 20% more energy than necessary due to faulty construction, malfunctioning equipment, incorrectly configured control systems and inappropriate operating procedures.” – Mediterranean Green Energy Forum
Can we identify faults/anomalies using machine learning techniques?

## Slide 3: High-Level Road Map
1. Manipulate Data to be Stationary
2. Create Forecasting Model
3. Obtain Residual Distribution
4. Flag Points with Z-Score above Threshold

## Slide 4: Step 1: Stationary Data
Forecasting techniques work the best when the data is stationary, in other words the mean and variance of the data should be constant.
Techniques such as transformations (typically log) and differencing are used.
We can test if the data is stationary using the Dickey-Fuller Test (Common Practice).

## Slide 5: Step 2: Forecasting Model
A forecasting model such as ARIMA will gives us a model that will predict the energy consumption for a given building by taking into account trend and seasonality.
Possible Univariate Forecasting Models:
  ARIMA
  S-ARIMA
  Holts Winter Method
  Moving Average
  Exponential Smoothing
  ANN/RNN
Evaluation Metrics: MSE, RMSE, MAE, MAPE

## Slide 6: Step 3: Obtain Residual Distribution
The difference between the forecast model’s prediction and the true value is the residuals.
These residuals follow a Gaussian distribution (by the Central Limit Theorem).
Residual Data

## Slide 7: Step 4: Flag Points with a Z-Score Above Threshold
Extremely large positive or negative residuals are unlikely and will have a highly negative or positive Z-Score Value.
Flag Points Above or below set Z-Score thresholds
Z-Score tells us the magnitude and direction of the anomaly
Anomalies
ALERTS DASHBOARD

## Slide 8: *Step 5: Alternative to Forecasting, Generalized Extreme Studentized Deviate Test (GESD) (+CART)
Method that uses robust statistical methods to determine anomalies. Has been applied to energy consumption data.
Uses the data points and statistics to give Z-scores to points, same threshold principle can be used
Ensemble Anomaly Detection

## Slide 9: *Step 6: Multivariate Time Series Anomaly Detection
Forecasting Models presented previously are to detect anomalies given only the time data (independent) and one dependent variable (energy usage)
With Multivariate Forecasting Models we can include additional information such as temperature, humidity, wind speed, etc.
Multivariate Forecasting Models:
  VARMA
  LSTM