## Slide 1: Building Energy Consumption Classification
Dr. Lewe
Kunal Sharma
Georgia Institute of Technology
AREOspace Design Lab

## Slide 2: Problem Statement
“Typical Buildings Consume 20% more energy than necessary due to faulty construction, malfunctioning equipment, incorrectly configured control systems and inappropriate operating procedures.” – Mediterranean Green Energy Forum

## Slide 3: Objective
Goal: Detect abnormal cases of energy usage of the 137 buildings on the Georgia Tech campus by classifying daily building energy consumption.
Abnormal Cases May Detect:
  Energy Mismanagement
  Overconsumption
  Electric Issues

## Slide 4: Data Collection
Energy Used by 134 Campus Buildings
Data Stored in Servers
Energy Data Used for Classification

## Slide 5: Methodology
To classify a building’s energy behavior we will consider its energy “fingerprint”.
The fingerprint is a polar plot of the energy usage of a building over 24 hours, plotted in 15 min intervals.
Building Energy Consumption

## Slide 6: Classification Types
Concentric
People
Scheduler
Reverse
Random
Building’s energy consumption is relatively constant throughout the day
Building uses more energy during work hours likely due to energy consumption by people.
Building uses scheduler machine. Sudden jumps and drops in energy usage at set time periods.
Building energy usage during non-work hours is much greater than the energy usage for the rest of the day.
Building energy behavior that is abnormal and does not have a clear pattern.

## Slide 7: Data Labelling
Machine learning algorithms perform well on pattern recognition (classification) problems given sufficient examples.
2,926 energy signatures were manually labelled for training purposes.
Building Type: Scheduler

## Slide 8: Model Selection
Initially, 7 Machine Learning models were selected for classification.
Decision Trees
K Nearest Neighbors
Support Vector Machine
Random Forest
Naïve Bayes
Artificial Neural Network
Logistic Regression

## Slide 9: Data Labelling
Machine learning algorithms perform well on pattern recognition (classification) problems given sufficient examples.
2,926 energy signatures were manually labelled for training purposes.
Building Type: Scheduler

## Slide 10: Artificial Data Generation
Generated functions that create artificial data to look similar to the original.
The random forest classifier achieved a 98.7% accuracy in classifying artificial data but only achieved a mere 7% accuracy when classifying real instances of classes.
Randomly generated plots do not accurately represent the true variation in the data.
Concentric
People
Scheduler
Reverse
Random

## Slide 11: Data Manipulation (Rotation)
We multiplied the dataset size by “rotating” or changing the time of each consumption record.
Rotated by some multiple of 15 mins between 2 hours before to 2 hours after the time of the original data.
This method improved the accuracy by about 2%.
Data Rotations
Original
Forward Rotation
Backward Rotation

## Slide 12: Data Manipulation (Adding Noise)
To create even more data we tried multiplying every 15 minute data point by a small number to create a slightly different energy signature.
However, this decreased the accuracy by 3% likely because it only added noise to the data.
Data became distorted, losing the nuances in the data that were key to classification.
Added Noise is Normally Distributed

## Slide 13: Unbalanced Dataset
It was difficult to evaluate the performance of the models because the data was heavily unbalanced.
The overwhelming majority of samples were “Concentric” or “People”.
Distribution
Training Data Type Distribution
Type
Count

## Slide 14: Highest Performing Models
Decision Trees
K Nearest Neighbors
Support Vector Machine
Random Forest
Naïve Bayes
Artificial Neural Network
Logistic Regression
68%
86%
88%
43%
86%
38%
41%

## Slide 15: Random Forest: Accuracy 86.71%
Sample Decision Tree Complexity
Confusion Matrix

## Slide 16: K Nearest Neighbor: Accuracy 85.38%
Accuracy for Various K Values
Confusion Matrix

## Slide 17: Artificial Neural Network: Accuracy 85.38%
Neural Network Architecture: [96, 30, 20, 10, 8, 5]
Confusion Matrix

## Slide 18: What is an Ensemble Model?
An ensemble model combines several base models in order to produce one optimal predictive model.
One of the ways this can be implemented is with a voted weighted average.

## Slide 19: Ensemble Model: Accuracy 89.04%
Confusion Matrix
Ensemble
Classifier
Random Forest
K Nearest Neighbor
Artificial Neural Network
Voting Model
Algorithm | Accuracy
Ensemble Classifier | 89.04%
Random Forest | 86.71%
KNN | 85.38%
ANN | 85.38%
Accuracy

## Slide 20: Data Filtered By Threshold (kwH)
Since small buildings were found to behave erratically, they were removed from the dataset at different thresholds.
At a threshold of 150kwH the accuracy achieved is 90.21%.

## Slide 21: Filtering Effect on Dataset Size
As expected the size of the dataset decreases as the threshold increases.

## Slide 22: Closing Remarks
Ensemble Machine Learning models can effectively classify time series energy data.
If this project was repeated, more time would be spent on initial data exploration for clearer definition of classification prototypes.
More specific classifiers can be developed to the classify below-threshold buildings filtered out of classification.
Regression models and statistical techniques can be applied to identify anomalies and predict energy usage.